## Slide 2: What is Open Fast Path (OFP)?
IP fast path incubation project between Nokia, Enea and ARM
  Developers and supporting staff active from all three companies
API’s towards hardware is based on ODP (Open Data Plane)
  Maximizes portability and software reuse
”Democratic” governance model
  Decisions made in weekly meetings and logged in the google docs
Organized as an Open source project
  Using open source software
  BSD license
  Source code on GitHub
  Mailing list, shared Google docs, weekly calls, Freenode chat etc
Notes: IP + UDP from Nokia ufp
TCP from freeBSD

## Slide 3: Why is an Open source IP fast path stack needed?
The amount of data that needs to be managed increases exponentially
  HW supports multiple 10G and 40G interfaces today, with 100G coming in a near future
  As the average device core count goes up, application scalability becomes more important
Many networking systems are built on Linux
  Linux TCP/IP stack is mainly developed for features, not for performance
  Limitations such as scheduling pre-emptions, timers, locks, RCUs, etc. impacts throughput and scalability
The Linux TCP/IP stack is complex and implemented in kernel space
  Feature extensions and modifications are difficult
Very few open source fast path alternatives available – none on ODP

## Slide 4: Why base the OFP stack on ODP?
Standardized data plane API to enable networking applications across any architecture
  Open support for ARM, Intel, MIPS, PowerPC, RTOS, Linux, bare metal
Designed to be an generic yet high performance data plane abstraction layer
  Lightweight without prescribing lower level processing structure which can be vendor specific
  Access and management of HW accelerators and classification
  Supports optional schedulers to provision easy management and traffic load balancing
Defined to enable high throughput user plane applications
  Run to completion
  Core isolation (only 1 work thread per core scheduled by ODP)
  Minimal use to no use of Linux APIs
Major TEM’s onboard - Nokia, Ericsson, Huawei, ZTE and others

## Slide 5: OFP Source code
New open-source code
  Developed by partners during the incubation stage
UDP, TCP, ICMP code was ported from libuinet (Userland FreeBSD port)
  Non-blocking event based API
  Focused on performance and scalability
  Tightly coupled to application
  Maintainability – Tracks evolution of FreeBSD
Highly scalable code for MAC and Route lookup tables
All structures and functions calls have an “ofp” prefix: ofp_socket(), struct ofp_sockaddr

## Slide 6
NICs
API
Interface configuration
ODP
Application
CLI
Packet processing
API
Routes, ARP
IPv4
IPv6
MAC
API
Configuration Packets Information
Open Fast Path components
Linux kernel
TAP
Netlink
API
API
ODP
Linux
ODP API
OFP
HW
Application
Notes: Command line interface (CLI): Internal Command Line Interface to configure and debug OIP-FP.
Packet handler: Received packet handling.
Init: ODP environment, and internal memory initialization.
Netlink: Copies routes and interfaces from Linux.
TUN/TAP: Communication with Linux kernel, slowpath.
Port configuration: Ethernet interface functionality.
Route, arp: Route and ARP functions.
Application API: Function calls for configuration, packet processing, logging, etc...
AVL and Radix trees: Functionalities to be used by other modules.
Socket: BSD style socket interface
Protocols: UDP, TCP, UDP6, ICMP implementation

## Slide 7: OFP System View
Ingress API
User/Default Dispatcher
Packets
Ctrl
HW / NICs
ODP API
Host OS (Linux)
ODP FW
ODP SW
TAP
Netlink
Socket Hook API
Socket Egress API
User Termination or Forwarding
Init API
Open Fast Path (OFP)
PKTIO
Interface Management
User ConfCode
buf = odp_queue_deq(queue);
or
buf = odp_schedule(&queue, ODP_SCHED_WAIT);
ODP
Linux
ODP API
OFP
HW
Application
Slow path
Route tables

## Slide 8: Open Fast Path multicore System View
NICs
Dispatcher
Ingress API
Socket/Hook API
User Termination or Forwarding
Init API
Open Fast Path (OFP)
PKTIO
Host OS (Linux)
ODP FW/HW
Core 1
Core 1
Core N
Core 2
Dispatcher
Ingress API
Socket/Hook API
User Termination or Forwarding
Init API
Open Fast Path (OFP)
Netlink
TAP
PKTIO
Dispatcher
Ingress API
Socket/Hook API
User Termination or Forwarding
Init API
Open Fast Path (OFP)
PKTIO
User ConfCode
….
….
ODP API
ODP SW
ODP API
ODP SW
ODP API
ODP SW
….
ODP
Linux
ODP API
OFP
HW
Application
Slow path
Route tables

## Slide 9: User application APIs
  Initiation of Open Fast Path
  Interface configuration
  Route and MAC table access
  Packet Ingress and Egress processing
  BSD/POSIX “like” socket interface:
    Legacy mode select/send/recv callback (NOT zero-copy)
    Signal event + custom sigval with odp_packet_t and socket
  Hooks for IP local, IP forwarding and protocol level extensible.
  Timer callbacks
  Statistics
  Packet capture

## Slide 10: Ingress Packet Processing
Ethernet
Vlan
IPv4/v6
ARP
IPv4 local hook API
IPv4 GRE
IPv4/v6 routing
IPv4/v6 output
IPv4 forward hook API
Transport(L4) classifier
UDP input
TCP input
ICMP
Send ARP request
Socket API
Update MAC table
Pre-classified
L2
L3
L4
User API
Packets Information
IPv4 Reassembly
Ingress API
Fallback to slowpath for unknown traffic
GRE hook API
IP, UDP, TCP, … classified by HW

## Slide 11: Egress Packet Processing
Socket/Egress API
IPv4 output
UDP output
TCP output
ICMP error
IPv6 output
IPv4 GRE tunneling
Ethernet
Vlan
IPv4 Fragmentation
Pre-classified
L2
L3
L4
User API
Packets Information

## Slide 12: Features implemented
Fast path protocols processing:
  Layer 4: UDP termination, TCP termination, ICMP protocol
  Layer 3
    ARP/NDP
    IPv4 and IPv6 forwarding and routing
    IPv4 fragmentation and reassembly
    VRF for IPv4
  Layer 2: Ethernet, VLAN
  GRE Tunneling
Routes and MACs synced from Linux
Integration with Linux Slow path IP stack
Command line interface
  Packet dumping and other debugging
  Statistics, ARP, routes, and interface printing
  Configuration of routes and interfaces with VRF support